## Slide 1: Notes on this document
This is the user manual for the main input file. The main input file gathers all the parameters you need to set up to use SpOCK.
In addition to this file, you also need to write the geometry file. For this, please refer to how_to_write_the_geometry_file.
More details for complex sections are given in separated documents:
how_to_write_the_geometry_file
how_to_compute_specular_points (optional)
how_to_write_the_attitude_file (optional)
how_to_write_the_f107_and_ap_files (optional)
how_to_use_ensembles (optional)
how_to_write_the_density_file (optional)
The main input file includes different sections to set up the simulation. Each page of this document corresponds to one section of the main input file. Some sections are optional (indicated at the top of the page). Each page contains a table:
first column: type of input
second column: the different options you have
third column: examples
and comments below the table.
In the folder Examples/main_input, there are two examples of main input files. ex_main_input_basic.txt shows how to use the most basic functionalities of SpOCK, which will probably be the case for most of the runs you want to make. ex_main_input_complex.txt is an example of more advanced features available in SpOCK.
Any questions or comments? Email me at cbv@umich.edu!

## Slide 2
#TIME |  | 
Initial epoch | Start date now n | 2017-01-01T12:00:00 or now 5
Final epoch | End date | 2017-01-02T12:00:00
Time step | Time step | 5
Initial epoch: if option now n: start propagation at the current time and ends it n hours later (n can be a decimal number). Then do not care
about the final epoch line (but do not remove it).
Initial epoch: if you choose to put a date (and not ‘now n’), follow the format: YYYY-MM-DDTHH:MM:SS. Same for final epoch.
Time step: in seconds
Important (bug): if running more than one satellite (see section #SPACECRAFT), then the duration of the propagation (final epoch – initial epoch) must be at least equal to one orbit.

## Slide 3
#SPACECRAFT |  | 
Number of satellites | Number of satellites | 2
Name of the GPS TLE file | Name of the GPS TLE file 0 | gps_2017-01-01.txt or 0
Mass | Mass of the spacecraft | 3
Solar cell efficiency | Solar cell efficiency -1 | 0.28 or -1
Geometry file name | Geometry file name ballistic_coefficient | cubesat_1u.txt or ballistic_coefficient
Number of satellites: now noted n. Does not include the number of GPS satellites (if any is run, see second line).
Name of the GPS TLE file: GPS satellites are initialized using a TLE file that contains the TLEs for all GPS. This file has to be in ./input/tle/constellation_gps_tle/. The format is the same as in https://celestrak.com/NORAD/elements/gps-ops.txt. Please make sure that the epochs of these TLEs are consistent with the initial epoch of the propagation (first line of section #TIME): the TLE epochs need to be older than (or equal to) the initial epoch of propagation. If you do not want to run GPS, then put 0 at the second line.
Mass: all satellites (except GPS of course) have the same mass. In kg.
Solar cell efficiency: all satellites have the same solar cell efficiency. Indicate -1 if you do not want to compute the solar power.
Geometry file name: see the document how_to_write_the_geometry_file.
The geometry file has to be in ./input/geometry/.
If ballistic_coefficient: this will read the Bstar term of the TLE and calculate a ballistic coefficient from it. This implies that you have to initialize the orbit with a TLE (see section #ORBIT). If you use ballistic_coefficient, then you can't compute solar power and you can't take into account the solar radiation pressure (since SpOCK does not know the geometry of the spacecraft).

## Slide 4
#ORBIT |  | 
Type of initialization | oe tle state_ecef state_eci deployment | oe or tle or state_ecef or state_eci or deployment
Orbit initialization | If oe: apogee_altitude(km) inclination(°) perigee_argument(°) RAAN(°) true_ano(°) ecc(°) If tle: Two Line Elements filename If state_ecef : position velocity (in ECEF) If state_eci : position velocity (in ECI) If deployment : apogee_altitude(km) inclination(°) perigee_argument(°) RAAN(°) true_ano(°) ecc(°) deployment_speed deployment_angle | Examples here are for 2 satellites: if oe: 500 35 0 70 12 0 450 85 45 20 0 0.01 if tle: ex_tle1.txt ex_tle2.txt if state (eci or ecef): (6878.137; 0; 0) (0; 1.1909; 7.5194) (6878; 780; 0) (2; 3; 2.191) if deployment: 500 35 0 70 12 0 1.0 30 500 35 0 70 12 0 1.0 270
Orbit initialization: one line per satellite (not the GPS satellites since their initialization is automatically made reading the TLE file (second line of section #SPACECRAFT (if not 0))). Exception: if ‘tle’ at first line then 2 options to initialize the orbit of each satellite. Either one tle file per satellite, in which case one line per filename. Or the tle of each satellite can all be included in the same file, in wchih case write the filename of this single tle file
All the distance-units are in km, except for the deployment speed (in m/s).
Orbit initialization with state (ECI or ECEF): make sure you write the state with the correct format: (x; y; z) (vx; vy; vz)
If deployment: orbital elements of the deployment module and deployment speed/angle of the satellites that are deployed from it.
An angle of for example 30 degrees is counted from the in-track direction to the right (clockwise, satellite seen from ‘the top’). For now we assume the satellites are deployed in in-track/cross-track plane (so not in the radial direction).
With the deployment example here, s1 is ejected from the deployment module (at a position given by the 6 oe) with a speed of 1 m/s making an angle of 30° with the in-track direction, and s2 is ejected with a speed of 1 m/s making an angle of 270° with the in-track direction from a position identical to s1 (so to to the left with an angle of 90° if satellites are seen from ‘behind’).

## Slide 5
#FORCES |  | 
Degree of the gravity model | Degree | 4
Forces to include | drag, solar_pressure, sun_gravity, moon_gravity | drag sun_gravity moon_gravity
Type of density drivers/density model | static dynamic density_file gitm | static or dynamic or density_file or gitm
F10.7 (value or file name) or omniweb or swpc or name of density file or path of GITM directory | Value of F10.7 (if static) Name of file F10.7 (if dynamic) omniweb (if dynamic) swpc (if dynamic) Name of density file (if density_file) Path of GITM directory that has the files (if gitm) | 150 or Example_F107_file.txt or omniweb or swpc or Example_density_file.txt or Path_to_gitm_directory/
F10.7A (value or file name) | Value of F10.7A (if static) Name of file F10.7A (if dynamic) | 150 or Example_F107A_file.txt
Ap (value or file name) | Value of Ap (if static) Name of file Ap (if dynamic) | 15 or Example_Ap_file.txt
Comments: see next slide.

## Slide 6
Perturbing forces: write ‘drag’, or ‘solar_pressure’, or ‘sun_gravity’, or ‘moon_gravity’ if you want to take into account the atmospheric drag, or the solar pressure, or the third body perturbations from the Sun or the Moon. In the example in the previous slide, all forces are computed except the solar radiation pressure. If you do not include drag, then do not care about the 4 following lines.
Type of density drivers:
static (uses NRLMSIS-00e model): next 3 lines indicate f10.7, f10.7A, Ap (1 per line, in this order).
dynamic (uses NRLMSIS-00e model): 3 options:
1- next line write ‘omniweb’ and don’t care about the 2 following lines
or
2- next line write ‘swpc’ and don’t care about the 2 following lines
or
3 - next 3 lines indicate the name of the files (1 per line, in the order filename_f107, filename_f107A, filename_ap). The files has to be in ./input/density/density_density_files/
density_file: indicate the name of the file on the next line, the 2 following lines will be ignored. The density file has to be in ./input/density/density_density_files/
gitm (uses GITM model): on the next line, indicate the path of the directory that has the GITM files (don't forget the last slash at the very end of the path). The 2 following lines will be ignored.

## Slide 7
#OUTPUT |  | 
Name of output folder | Name or out | my_first_run
Output time step | Output time step in seconds | 30
Name of output folder: a folder with this name is created in ./output. In this folder, n subfolders are created (n: number of satellites (first line of section #SPACECRAFT)). Each subfolder includes the outputs of the satellite.
In the example here, if 2 satellites are run then the following folders will be created:
./output/my_first_run/my_first_run1/ and ./output/my_first_run/my_first_run2/.
If GPS are run (second line of section #SPACECRAFT) then all GPS positions are gathered in a subfolder constellation_GPS (./output/my_first_run/constellation_GPS/ in the example).
If the name is ‘out’ then the folder will be named the same as the name of the input file (without the file extension (‘.txt’ for example)). So for instance if the name of the main input file is ex_main_input_basic.txt, and the user puts ‘out’ at the first line of section #OUTPUT, the output folder is called ‘ex_main_input_basic’.
Output time step: time step to write the output of the propagator (positions, velocities, orbital elements, power, etc). This time step has to be greater than the integration time step (third line of section #TIME), and a multiple of it.

## Slide 8
#GROUND_STATIONS (optional) |  | 
File name for the ground stations | Name of the file | My_ground_stations.txt
This section can compute the coverage of the n satellites above ground stations.
This file includes the position and minimum elevation angle of all the ground stations.
This file has to be in ./input/coverage/ground_station/.
How to write the file (example):
#BEGINNINGOFHEADER
put optional header here
#ENDOFHEADER
- Line below #ENDOFHEADER:#START
- Lines below #START: ground stations. One per line, following the format:
name_of_ground_station(no space) latitude(deg) longitude(deg) altitude(m) min_elevation_angle(deg)
- Line below the last ground station:#END
Example:
#BEGINNINGOFHEADER
This is a header
#ENDOFHEADER
#START
hawaii 21. -157. 0 5
chile -33. -70. 0 5
australia -31. 115. 0 5
#END
For each satellite, a subfolder coverage/ is created. One file per ground station. It includes the azimuth and elevation angles in both the ground station and the spacecraft reference systems, as well as the range, for every second of the propagation. A summary report (one file for all ground stations) is also created that shows the access start and end times when the spacecraft flies over the ground station, in the half cone defined by the minimum elevation angle. To get this summary report, run the python script ./srcPython/report_coverage_ground_station.py (see explanations in the header of this script).
If this section is not included, then the number of ground stations is set to 0 by default.

## Slide 9
#ATTITUDE (optional) |  | 
Type of attitude | nadir sun_pointed name of external file ensemble_angular_velocity ensemble_initial_attitude (pitch_ang_velo; roll_ang_velo; yaw_ang_velo) | nadir or sun_pointed or Example_attitude_file.txt or ensemble_angular_velocity or ensemble_initial_attitude or (2.0; 1.0; 1.3)
nadir: the satellites are constantly nadir pointing: x_body in the in-track direction, z_body in the radial direction (oriented away from the Earth), y_body in the cross-track direction
sun_pointed: the satellites are constantly Sun pointing: z_body in the direction of the Sun.
If option ‘name of external file’: please see the document how_to_write_the_attitude_file.
If option ‘ensemble_angular_velocity’ or ‘ensemble_initial_attitude’: please see document how_to_use_ensembles.docx
If choose to input (pitch_ang_velo; roll_ang_velo; yaw_ang_velo): in degree/s. The order of rotation is: pitch then roll then yaw.
Same attitude for all satellites.
If there is no section #ATTITUDE, then nadir pointing is assumed by default.

## Slide 10
#SPICEFILES (optional) |  | 
Names of SPICE files to load | Default or name of earth binary pck file | default or string1_string2_YYMMDD_string3.bpc
These are the files that the propagator loads that includes ephemerides of the Sun and planets/moons, leap seconds, etc.
Only two options: default or the name of the the Earth binary pck file (used for Earth body-fixed rotating frame for conversion from ECI to ECEF coordinates).
If default, then the following files are loaded:
naif0011.tls, pck00010.tpc, de430.bsp, earth_000101_160830_160608.bpc
In the example, if you don’t write default but string1_string2_YYMMDD_string3.bpc then the folllowing files will be loaded: naif0011.tls, pck00010.tpc, de430.bsp, string1_string2_YYMMDD_string3.bpc
If other than ’default ’, the name of the file must have the format string1_string2_YYMMDD_string3.bpc.
Important: these spice files have to be in directory_to_cspice/data/ (where directory_to_cspice is indicated in the Makefile at SPICE_DIR).
If the user does not include this section in the main input file then the following files are loaded the default option` is used (this right above).

## Slide 11
##ENSEMBLES_COE (optional) |  | 
Total number of ensembles | Total number of ensembles | 1000
Standard deviation on the orbital elements | apogee altitude, inclination, argument of perigee, RAAN, true anomaly, and eccentricity | Example with 2 satellites: 10.0 0.0 20.0 0.0 0.0 0.0 10.0 30.0 0.0 0.0 0.0 0.0
Please see the document how_to_use_ensembles.
If you run ensembles on the orbital elements, then at the section “#ORBIT”, you need to initialize the orbit with orbital elements as well.
One line per satellite.
Looking at the example (and the example of the section #ORBIT), the first 1000 ensembles for the first main satellite will correspond to 1000 satellites with altitudes normally distributed around 500 km with a standard deviation of 10 km, and an argument of perigee around 0° with a standard deviation of 20°. The 1000 ensembles for the second main satellite will correspond to 1000 satellites with altitudes normally distributed around 450 km with a standard deviation of 10 km, and an inclination around 85° with a standard deviation of 30°.
If this section is not included in the main input file then no ensembles on the orbital elements are run.

## Slide 12
##ENSEMBLES_ATTITUDE (optional) |  | 
Number of ensembles for the attitude | Number of ensembles for the attitude | 1000
If this section is not included in the main input file then no ensembles on the attitude are run.

## Slide 13
###ENSEMBLES_ANGULAR_VELOCITY (optional) |  | 
Delay before going back to the nominal attitude | delay | 300
standard deviation on the the angular velocity | (sigma pitch ang velo; sigma roll ang velo; sigma yaw ang velo) | (0.033; 0.033; 0.033)
Please see the document how_to_use_ensembles.
This section is to model an Attitude Determination and Control System (ADCS). For now, this section here works if there is only one satellite in the constellation (first line of section #SPACECRAFT).
Every x seconds (x is the delay), the satellites go back to the nominal attitude indicated in the section #ATTITUDE. Then, they drift for x seconds with initial angular velocities distributed normally around 0 rad/s and standard deviations defined on the second line.
Delay: In seconds.
Standard deviation: in degree/s.
Following the example here, every 5 minutes the 1000 satellites will go back to the nominal attitude chosen at section #ATTITUDE. Then they drift with random pitch, raw, and yaw angular velocities distributed following a normal distribution with a standard deviation of of 0.033 degrees/s and a mean of 0 degree/s.
Note: if you want to use this section then the section ##ENSEMBLES_ATTITUDE needs to be included in the main input file as well.

## Slide 14
###ENSEMBLES_ANGULAR_VELOCITY_DEPLOYMENT (optional) |  | 
initial attitude (pitch; roll; yaw) | initial attitude (pitch; roll; yaw) | (20; 10; 0)
Mean of the normal distribution on the initial angular velocities | (pitch angular velocity; roll angular velocity; yaw angular velocity) | (0; 0; 0)
Standard deviation of the normal distribution on the initial angular velocities | (pitch angular vel sigma; roll angular vel sigma; yaw angular vel sigma) | (1; 1; 1)
To use this section, you need to put ensemble_angular_velocity in section #ATTITUDE.
Please see the document how_to_use_ensembles.
This section is to represent an uncertainty on the initial angular velocity (at the deployment for example). For now, this section here works if there is only one satellite in the constellation (first line of section #SPACECRAFT).
Initial attitude: at the first time step, the ensembles start with the same attitude. Example here: 20° pitch, 10° roll, no yaw.
Initial angular velocity: in the example here, the attitude of the ensembles have an initial pitch/roll/yaw angular velocities that follow a normal distribution centered around 0 degree/s (second line) with standard deviations of 1 degree/s (third line).
Note: if you want to use this section then the section ##ENSEMBLES_ATTITUDE needs to be included in the main input file as well.

## Slide 15
###ENSEMBLES_INITIAL_ATTITUDE (optional) |  | 
Mean of the normal distribution on the initial attitude (pitch; roll; yaw) | (mean pitch; mean roll; mean yaw) | (20; 10; 0)
Standard deviation of the normal distribution on the initial attitude | (std pitch; std roll; std yaw) | (2; 3; 1)
Initial angular velocity | (pitch ang velo; roll ang velo; yaw ang velo) | (1; 4; 9)
To use this section, you need to put ensemble_initial_attitude in section #ATTITUDE.
Please see the document how_to_use_ensembles.
This section is to represent an uncertainty on the initial attitude, assuming the angular velocity is perfectly known. For now, this section here works if there is only one satellite in the constellation (first line of section #SPACECRAFT).
Initial attitude: at the first time step, the ensembles ensembles have an initial pitch/roll/yaw that follow a normal distribution centered around 20° (pitch), 10° (roll), 0° (yaw) (first line) with standard deviations of 1° (pitch), 3° (roll), 1° (yaw) (second line).
Initial angular velocity: in the example here, , the attitude of the ensembles start with the same angular velocity: 1°/s for pitch ang velo, 4°/s for roll ang velo, 9°/s for yaw ang velo.
Note: if you want to use this section then the section ##ENSEMBLES_ATTITUDE needs to be included in the main input file as well.

## Slide 16
#OUTPUT_ENSEMBLES (optional) |  | 
parameter you want to output for the ensembles | - eci_r - eci_v - geodetic - oe - attitude - power | eci_r, geodetic
Please see the document how_to_use_ensembles.

## Slide 17
#STORMS (optional) |  | 
Number of storms | Number of storms | 1
file names for each storm | Name of the storm file | Joaquin.dat
This section can compute the coverage of the n satellite above x storms. This was originally done for CYGNSS. But now for CYGNSS, we are interested in the coverage of the specular points, not the satellites themselves.
This file has to be in input/coverage/storm.
For more information, please refer to the file how_to_compute_spcular_points_positions_and_coverage_of_storms.docx.
If this section is not included, then the number of storms is set to 0 by default.